Video And Computer
Projection In
Axinn Center 100

#### Library and Information Services

Revised June 17, 2008

Video And Computer Projection In
Axinn Center 100

Table Of Contents

# Location Of Equipment

Axinn Center 100 is equipped with a projection system that accepts input from multiple laptop computers, a VCR, a DVD player, a Laserdisc player, and auxiliary video equipment and projects the output onto the screen at the front of the room for display. All equipment is controlled by the Touch Panel system. The relevant equipment is located at:

| Equipment | Location |
| --- | --- |
| Touch Panel | A small screen on top of the lectern |
| Projector | Hanging from the ceiling |
| Projection screen | In ceiling pocket at the front of the room |
| Computer network cable | Cable plugs into wall behind lectern |
| Computer interface cables | On the lectern (labeled Laptop 1 and Laptop 2) |
| VCR | In the lectern |
| DVD player | In the lectern |
| Auxiliary equipment adaptors | In the lectern |

# Using The Touch Panel

The control system for audio-visual equipment in this room is incorporated in the Touch Panel system.  An overview of your interaction with the Touch Panel system is:

- Touch the Touch Panel screen anywhere to activate it.  Note that you should use a deliberate pressing motion when interacting with the controls rather than a light tap or a hard jab.

- When the Axinn Center 100 screen appears, touch the Touch Panel screen anywhere to access the main menu.

- Touch the button for the equipment you want to use.  Control the equipment you want to use with the Touch Panel system, including room lights, projection screen, VCR, your laptop computer, DVD/CD player, and auxiliary computer and video equipment. From most control screens you can also:

- Touch  to lower or raise the projection screen.

- Touch  or  to increase or decrease the level of sound.

- Touch  to return to the main menu to access the Shutdown procedure.

- When you are finished:

  - Touch , then touch  to end your session.  The Shutdown Warning displays.

  - Touch  to end your session or touch  if you’ve started the shutdown process by mistake.
Note:  You cannot turn the projection system back on for 3 minutes after shutdown.

Notes:  It is important that everything is turned off to protect the integrity of the security system and extend the life of the electronic equipment.
You must remove your media from the equipment BEFORE you turn off the system power.

# Screen Controls

- On any screen, touch .

- Touch  or  to raise or lower the screen.

# Room Light Controls

The room lights are controlled by the set of switches near the door.

# Projection From Your Computer

It is critical to the success of projecting a computer image that you follow this procedure in the order outlined below.

- Connect your computer to one of the computer input cables sets on top of the lectern.
Please note that your computer should be in full shutdown mode (not in Sleep mode) when you make cable connections.

- Projection of the computer image requires the 15-pin cable.

- Computer sound amplification requires the mini-stereo cable which is part of the above cable.

- If you need network access, plug your computer into the network cable that plugs into the red network jack.

- Follow steps 1-3 in the section Using The Touch Panel.

- Touch  or  on the touch panel main menu depending upon which cable you connected your computer to.

- Start your computer (note that a Macintosh G3 must be started after the projection system).

- If the projection screen has an error message on it saying INPUT A NO INPUT, see the section What To Do If Your Computer Doesn’t Project.

- If your computer projects on the screen but you cannot access the network, see the section What To Do If Your Windows Computer Can’t Access The Network.

- Computer sound volume is increased or decreased each time you touch  or .

- When you are finished, please return the room to its former condition:

  - Touch , then touch  to end your session.  The Shutdown Warning displays.

  - Touch  to end your session or touch  if you’ve started the shutdown process by mistake.
Note:  You cannot turn the projection system back on for 3 minutes after shutdown.

Notes:  It is important that everything is turned off to protect the integrity of the security system and extend the life of the electronic equipment.

## What To Do If Your Computer Doesn’t Project

You may have to manipulate your computer so it will send its display to the projection system:

### On A Windows Computer

Press and hold  and press the function key that controls monitor selection to cycle between input options.  The function key is , , , , or  on most PCs — it will be marked with CRT/LCD or a monitor icon ( or ).  The input options are:

- Video output going to the computer monitor only.

- Video output going to the computer monitor and to the projection screen.

- Video output going to the projection screen only.

### On A Macintosh Computer Using OS X

- Click  on the docking station.  The System Preferences window opens.

- Click .  The Color LCD window displays.

- In the Resolution field, you will see a variety of resolution options.  Click to select one of the options.  
Note:  There may be several options including 640 x 480, 800 x 600, and 1024 x 768.  Do not select anything larger than 1024 x 768, the larger the number, the smaller the image projected.  Anything above 1024 x 768 will not be easily readable.

- Click the close button to close the Color LCD window.

## What To Do If The Projected Image Does Not Look As It Should

If the screen has no image, or the image is off-center or the color of the desktop image is not what is expected, touch  on the Computer control page.

## What To Do If Your Macintosh OS X Computer Can’t Access The Network

  - Click  on the Dock.  The System Preferences window opens.

  - Click .  The Network control panel opens.

  - From the Show drop-down list, select Built-in Ethernet.

  - Click .

  - Close the System Preferences window.

## What To Do If Your Windows Computer Can’t Access The Network

TCP/IP based services (such as web access), require your laptop to have an IP address which it gets by querying Middlebury’s DHCP server during startup.  The server gives the querying computer a set of configuration parameters valid for the location of the computer called a lease, which it can use for a set period of time.  When the lease expires, the Windows computer requests a new lease.

When you move a laptop with a valid lease from one sub-network to another it will not request new data from the server and the data may be invalid for your new location.  For instance, in Bicentennial Hall, each floor is in a different subnet and computers must have different configuration parameters.  So you should perform the following procedure whenever you move your computer from one location to another even if you think you have not changed sub-networks.

- Click  and select Run from the pop-up menu; the Run dialog box will open.

- In the Open text box, type command.

- Click .  The command.com window opens.

- Release and renew IP information for all adaptors on a Windows NT, Windows 2000, or Windows XP computer:

  - At the prompt, type ipconfig /release and press .

  - At the prompt, type ipconfig /renew and press .

  - At the prompt, type exit and press .  The command.com window closes.

# Projection From The DVD Player

- Follow steps 1-3 in the section Using The Touch Panel.

- Touch  on the menu.  The DVD Player menu displays.

- Press Open/Close on the DVD player and load the media into the player.

- Press Open/Close on the DVD player again to close it.

- Several buttons on the DVD Controls menu help you control the viewing of your video.

- reverses the DVD by one chapter; each touch of the button reverses play by one chapter.

- touch to play in reverse.

- begins play.

- pauses the DVD leaving the image on the screen.

- One touch of  stops the DVD and projects a medium blue blank image on the screen. The DVD will restart from the point where you stopped. To cancel the resume feature, touch  again.

- touch to fast forward.

- fast-forwards the video by chapter; each touch forwards by one chapter.

  - Sound volume is increased or decreased by touching  or  on the Touch Panel.

  - To activate the DVD menu, touch , the menu on the disc will display on the projection screen.

    - Touch the directional buttons (, , , or ) to move around the menu.

    - Touch  to select a highlighted menu item.

- Remove the DVD by pressing Open/Close on the DVD player.

- When you are finished:

- Touch , then touch  to end your session.  The Shutdown Warning displays.

- Touch  to end your session or touch  if you’ve started the shutdown process by mistake.
Note:  You cannot turn the projection system back on for 3 minutes after shutdown.

Notes:  It is important that everything is turned off to protect the integrity of the security system and extend the life of the electronic equipment.
You must remove your media from the equipment BEFORE you turn off the system power.

# Projection From The VCR

- Follow steps 1-3 in the section Using The Touch Panel.

- Touch  on the menu.  The VHS Deck menu displays.

- Load the video into the VCR; it begins to play automatically, if the cassette’s tab is broken.

- Several buttons on the menu help you control the viewing of your movie.

- reverses the video.

- If you want a medium blue blank image projected onto the screen during reverse play, touch , then .

- If you want to scan the video in fast reverse and have it display on the screen, touch  while the video is in Play mode.

- begins video play.

- pauses the video leaving the image on the screen.

- stops the video and projects a medium blue blank image on the screen.

- performs a fast-forward scan of the video.

- If you want a medium blue blank image projected onto the screen during forward scan, touch , then  (you can monitor progress with the time indicator on the VCR).

- If you want to scan the video in fast forward and have it display on the screen, touch  while the video is in Play mode.

- Sound volume is increased or decreased by touching  or , on the Touch Panel.

- Remove the video by pressing  (Eject) on the VCR.

- When you are finished:

  - Touch , then touch  to end your session.  The Shutdown Warning displays.

- Touch  to end your session or touch  if you’ve started the shutdown process by mistake.
Note:  You cannot turn the projection system back on for 3 minutes after shutdown..

Notes:  It is important that everything is turned off to protect the integrity of the security system and extend the life of the electronic equipment.
You must remove your media from the equipment BEFORE you turn off the system power.

# Projection From Auxiliary Equipment

A special set of input receptacles is located in the equipment rack inside the lectern.  Use them to connect other audio/visual sources such as U-Matic, Beta or multi-standard type VCRs such as PAL or SECAM compatibles.  The projectors are compatible with all current video standards.

- Connect your equipment using special audio and video interconnection cables (contact Media Services) to a special set of receptacles located in the lectern.

- Refer to the device manual for set-up and operating instructions.

- Follow steps 1-3 in the section Using The Touch Panel.

- Touch  to use an auxiliary video source.  A pop-up menu with several options displays.  You may choose from the following:

- Sound volume is increased or decreased by touching  or , on the Touch Panel.

- When you are finished:

  - Touch , then touch  to end your session.  The Shutdown Warning displays.

- Touch  to end your session or touch  if you’ve started the shutdown process by mistake.
Note:  You cannot turn the projection system back on for 3 minutes after shutdown..

Notes:  It is important that everything is turned off to protect the integrity of the security system and extend the life of the electronic equipment.
You must remove your media from the equipment BEFORE you turn off the system power.

# Trouble Shooting

| If there is no picture: | Reselect the input device on the Touch Panel system. Computers may require using . |
| --- | --- |
| If there is no sound: | Reselect the input device on the Touch Panel system. Adjust the volume on the device you are using by touching several times. |

# Getting Help

Call the Helpdesk at x2200 for assistance with problems in this classroom.